## Slide 1: Coordinate Geometry COGO

## Slide 2
Computations for determining
  Positional relationships between coordinate pairs.
  Using trig to solve point positions
COGO
N
(N, E)
a
L
N=?
E=?
a=?
L=?
(N, E)
(N, E)
N

## Slide 3
Based on plane trigonometry; emphasis on triangle solutions.
Computations limited to plane surveying which simplifies them.
COGO
B
A
C
b
a
c

## Slide 4
A reference system (datum) for expressing horizontal positions
A. Coordinates
  1. Definition

## Slide 5
A reference system (datum) for expressing horizontal positions
A. Coordinates
  2. Characteristics
Two reference axes
Perpendicular
Uniform scaling

## Slide 6
Absolute position expressed by perpendicular linear distances from the axes.
A. Coordinates
  3. Position
    a. Absolute
  X and Y axes
Y
X
XA
YA
(0,0)

## Slide 7
Absolute position expressed by perpendicular linear distances from the axes.
A. Coordinates
  3. Position
    a. Absolute
North and East axes
North
East
EA
NA
(0,0)
A (NA, EA)

## Slide 8
Absolute position expressed by perpendicular linear distances from the axes.
A. Coordinates
  3. Position
    a. Absolute
We’ll use North-East (N,E) coordinate nomenclature
North
East
EA
NA
(0,0)
NB
EB
A (NA, EA)
B (NB, EB)

## Slide 9
Relative position is distance and direction from one point to another
A. Coordinates
  3. Position
    a. Relative
North
East
(0,0)
A
B
LAB & DirAB

## Slide 10
Computing coords (absolute) from dist and dir (relative)
A. Coordinates
  4. Forward Computation
North
East
(0,0)
A (NA, EA)
B (?, ?)
LAB & DirAB
Must have a starting coordinate

## Slide 11
Computing coords (absolute) from dist and dir (relative)
A. Coordinates
  4. Forward Computation
Latitude (Lat)
  N/S line component
    N is (+), S is (-)
Departure (Dep)
  E/W line component
    E is (+), W is (-)
A (NA, EA)
North
East
(0,0)
B (?, ?)
LAB & DirAB
LatAB
DepAB

## Slide 12
Computing coords (absolute) from dist and dir (relative)
A. Coordinates
  4. Forward Computation
Lat = L x cos(Dir)
Dep = L x sin(Dir)
North
East
(0,0)
A (NA, EA)
B (?, ?)
LAB
LatAB
DepAB
DirAB

## Slide 13
Computing coords (absolute) from dist and dir (relative)
A. Coordinates
  4. Forward Computation
Lat = L x cos(Dir)
Dep = L x sin(Dir)
NB = NA +LatAB
EB = EA + DepAB
North
East
(0,0)
A (NA, EA)
B (NB, EB)
LatAB
DepAB
LAB
DirAB

## Slide 14
Computing coords (absolute) from dist and dir (relative)
A. Coordinates
  4. Forward Computation
0° ≤ Brng ≤ 90°
Lat = L x cos(Brng)  (+)
Dep = L x sin(Brng)  (+)
Lat & Dep sign det’d by Brng quad
N
E
S
W
Brng
Brng
Brng
Brng
+Lat
+Dep
-Lat
+Dep
+Lat
-Dep
-Lat
-Dep

## Slide 15
Computing coords (absolute) from dist and dir (relative)
A. Coordinates
  4. Forward Computation
0° ≤ Az ≤ 360°
Lat = L x cos(Az)
Dep = L x sin(Az)
Using Az results in correct sign for Lat & Dep
N
E
S
W
Az
Az
Az
Az
+Lat
+Dep
-Lat
+Dep
+Lat
-Dep
-Lat
-Dep

## Slide 16
Computing coords (absolute) from dist and dir (relative)
Lat & Dep Example:
    Line AB: 156.39 S35°18’20”E
      Lat =
      Dep =
    Line ST: 203.66 Az 235°23’50”
      Lat =
      Dep =
A. Coordinates
  4. Forward Computation
A
B
S
T

## Slide 17
Computing coords (absolute) from dist and dir (relative)
Lat & Dep Example:
    Line AB: 156.39 S35°18’20”E
      Lat = 156.39 x cos(35°18’20”) = 127.627  -127.627
      Dep = 156.39 x sin(35°18’20”) = 90.384  +90.384
    Line ST: 203.66 Az 235°23’50”
      Lat =
      Dep =
A. Coordinates
  4. Forward Computation
A
B
S
T

## Slide 18
Computing coords (absolute) from dist and dir (relative)
Lat & Dep Example:
    Line AB: 156.39 S35°18’20”E
      Lat = 156.39 x cos(35°18’20”) = 127.627  -127.627
      Dep = 156.39 x sin(35°18’20”) = 90.384  +90.384
    Line ST: 203.66 Az 235°23’50”
      Lat = 203.66 x cos(235°23’50”) = -115.655
      Dep = 203.66 x sin(235°23’50”) = -167.634
A. Coordinates
  4. Forward Computation
A
B
S
T

## Slide 19
to minus from
DE
DN
LCD
C
D
a
Computing dist and dir from coords
A. Coordinates
  5. Inverse Computation
DN = LatCD = ND-NC
DE = DepCD = ED-EC

## Slide 20
 | Algebraic sign of: |  |  |  | 
Quad | ΔN | ΔE | α | Bearing | Azimuth
NE | + | + | + | N α E | α
SE | – | + | – | S ¦ α ¦ E | 180°+ α
SW | – | – | + | S α W | 180°+ α
NW | + | – | – | N ¦ α ¦ W | 360°+ α
Computing dist and dir from coords
A. Coordinates
  5. Inverse Computation
N
E
S
W
"
"
"
"

## Slide 21
Computing dist and dir from coords
Example: Length and direction of Q to W
A. Coordinates
  5. Inverse Computation
Point | North (ft) | East (ft)
Q | 833.77 | 310.41
W | 418.61 | 548.01
Q
W
DN =
DE =

## Slide 22
Computing dist and dir from coords
Example: Length and direction of Q to W
A. Coordinates
  5. Inverse Computation
Point | North (ft) | East (ft)
Q | 833.77 | 310.41
W | 418.61 | 548.01
Q
W
DN = 418.61 – 833.77 = -416.16
DE = 548.01 – 310.41 = +237.60

## Slide 23
Computing dist and dir from coords
Example: Length and direction of Q to W
A. Coordinates
  5. Inverse Computation
Point | North (ft) | East (ft)
Q | 833.77 | 310.41
W | 418.61 | 548.01
Q
W
DN = 418.61 – 833.77 = -416.16
DE = 548.01 – 310.41 = +237.60

## Slide 24
Computing dist and dir from coords
Example: Length and direction of Q to W
A. Coordinates
  5. Inverse Computation
Point | North (ft) | East (ft)
Q | 833.77 | 310.41
W | 418.61 | 548.01
Q
W
DN = 418.61 – 833.77 = -416.16
DE = 548.01 – 310.41 = +237.60
E
S

## Slide 25
Computing dist and dir from coords
Example: Length and direction of Q to W
A. Coordinates
  5. Inverse Computation
Point | North (ft) | East (ft)
Q | 833.77 | 310.41
W | 418.61 | 548.01
Q
W
DN = 418.61 – 833.77 = -416.16
DE = 548.01 – 310.41 = +237.60
E
S
BrngQW = S 29°43’25”E
AzQW = 180°00’00”-29°43’25”
= 150°16’35”
Brng
Az

## Slide 26
Angle condition
  A + B + C = 180°00’00”
Law of Sines
Law of Cosines
Area
B. Plane Trigonometry
  1. Triangle formulae
B
A
C
b
a
c

## Slide 27
Both have same angles
A triangle has three angles and three sides.
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae

## Slide 28
a
b
B
A
C
c
a
b
B
A
C
c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae

## Slide 29
Law of Cosines
a2 = b2 + c2 - 2 x(bc)xCos(∠A)
a
b
B
A
C
c
a
b
B
A
C
c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae

## Slide 30
Law of Cosines
a2 = b2 + c2 - 2 x(bc)xCos(∠A)
Can then use either Law of Cosines or Sines to solve the remaining parts.
a
b
B
A
C
c
a
b
B
A
C
c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae

## Slide 31
Law of Cosines
a2 = b2 + c2 - 2 x(bc)xCos(∠A)
a
b
B
A
C
c
a
b
B
A
C
c
Law of Cosines
a2 = b2 + c2 - 2 x(bc)xCos(∠A)
Can then use either Law of Cosines or Sines to solve the remaining parts.
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae

## Slide 32
Law of Cosines
a2 = b2 + c2 - 2 x(bc)xCos(∠A)
Can then use either Law of Cosines or Sines to solve the remaining parts.
a
b
B
A
C
c
a
b
B
A
C
c
Law of Cosines
a2 = b2 + c2 - 2 x(bc)xCos(∠A)
Can then use either Law of Cosines or Sines to solve the remaining parts.
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae

## Slide 33
a
b
B
A
C
c
a
b
B
A
C
c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae

## Slide 34
Start with the angle condition
180° = ∠A + ∠B + ∠C
a
b
A
C
c
a
b
B
A
C
c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
B

## Slide 35
Then Law of Sines to solve another side.
Then Law of Cosines or Sines to solve the remaining side.
a
b
A
C
c
a
b
B
A
C
c
Start with the angle condition
180° = ∠A + ∠B + ∠C
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
B

## Slide 36
Sin(∠A) Sin(∠C)
=
a c
Start with Law of Sines
Then Law of Sines to solve another side.
Then Law of Cosines or Sines to solve the remaining side.
a
b
A
C
c
a
b
B
A
C
Start with the angle condition
180° = ∠A + ∠B + ∠C
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
B
c

## Slide 37
Start with Law of Sines
Then angle condition to solve last angle.
Then Law of Sines to solve the last side.
Then Law of Sines to solve another side.
Then Law of Cosines or Sines to solve the remaining side.
a
b
A
C
c
a
b
B
A
C
Start with the angle condition
180° = ∠A + ∠B + ∠C
Sin(∠A) Sin(∠C)
=
a c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
c
B

## Slide 38
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
a
b
A
C
c
a
b
B
A
C
c
B

## Slide 39
Sin(∠B) Sin(∠C)
=
b c
Start with Law of Sines
a
b
A
C
c
a
b
B
A
C
c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
B

## Slide 40
Start with Law of Sines
Then angle condition to solve last angle.
Then Law of Sines to solve the last side.
Sin(∠B) Sin(∠C)
=
b c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
a
b
A
C
c
a
b
B
A
C
c
B

## Slide 41
?
Start with Law of Sines
Then angle condition to solve last angle.
Then Law of Sines to solve the last side.
Sin(∠B) Sin(∠C)
=
b c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
a
b
A
C
c
a
b
B
A
C
c
B

## Slide 42
Can’t be solved.
Start with Law of Sines
Then angle condition to solve last angle.
Then Law of Sines to solve the last side.
Sin(∠B) Sin(∠C)
=
b c
In order to geometrically fix the triangle you must start with at least three parts and one of those must be a side.
B. Plane Trigonometry
  1. Triangle formulae
a
b
A
C
c
a
b
B
A
C
c
B

## Slide 43
-1.0
-0.5
0.0
0.5
1.0
Sine
-180
-90
0
90
180
270
360
450
Angle, in degrees
Sine Curve
  Sine Curve
    This curve repeats itself every 360°.
    The sine of any angle falls between -1 and +1.
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine

## Slide 44
  The inverse sine of a number between -1 and +1 on a calculator will always return an angle between –90° and +90°.
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine
-1.0
-0.5
0.0
0.5
1.0
Sine
-180
-90
0
90
180
Angle, in degrees
Angle | x = sin(Angle) | sin-1(x) | relationship
30° | +0.500000 | +30° | Angle
150° | +0.500000 | +30° | 180° - Angle
210° | -0.500000 | -30° | 180° - Angle
330° | -0.500000 | -30° | 360° + Angle

## Slide 45
  To solve a triangle using the law of sines you must have either:
    two angles and a side, or,
    two sides and an angle
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine
B
A
C
b
a
c

## Slide 46
  Example
    For a triangle ABC, a = 12.4', b = 8.7', and B = 36°40'.
    Compute the remaining angles and side.
    From Law of Sines
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine

## Slide 47
-1.0
-0.5
0.0
0.5
1.0
0
90
180
270
360
Sine Curve
+0.85112
58°20’
121°40’
Example
    There are two angles whose sine is +0.85112:
      A1 = 58°20’
      A2 = 180°00’ – 58°20’ = 121°40’
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine
12.4'
36°40'
8.7'
8.7'
B
C
A2
A1

## Slide 48
12.4'
36°40'
8.7'
B
C1
A
1
C
A
14.5'
  Example
    For A1 = 58°20’
    C1 = 180°00’-(36°40’+58°20’)
    = 85°00’
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine

## Slide 49
12.4'
36°40'
8.7'
B
C2
A2
C
A
5.4'
  Example
    For A2 = 121°40’
    C2 = 180°00’-(36°40’+121°40’)
    = 21°20’
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine

## Slide 50
  Example
    Compute the value of angle β:
    (1) By Law of Sines
    (2) By angle condition
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine
48°
24°
b
158.4 ft
123.8 ft

## Slide 51
  Example
    Compute the value of angle β:
    (1) By Law of Sines
    (2) By angle condition
B. Plane Trigonometry
  2. Trigonometric functions
    a. Sine
Be careful using the Law of Sines to solve for an unknown angle – there could be two possible answers only one of which will fit the particular triangle.
48°
24°
b
158.4 ft
123.8 ft

## Slide 52
-1.0
-0.5
0.0
0.5
1.0
Cosine
-180
-90
0
90
180
270
360
450
Angle, in degrees
Cosine Curve
  This curve repeats itself every 360°.
  The cosine of any angle falls between -1 and +1.
B. Plane Trigonometry
  2. Trigonometric functions
    b. Cosine

## Slide 53
-1.0
-0.5
0.0
0.5
1.0
Cosine
0
90
180
270
360
Angle, in degrees
Angle | x = cos(Angle) | cos-1(x)
60° | +0.500000 | +60°
300° | +0.500000 | +60°
120° | -0.500000 | +120°
-240° | -0.500000 | +120°
  The inverse cosine of a number between +1 and -1 on a calculator will always return an angle between 0° and +180°.
B. Plane Trigonometry
  2. Trigonometric functions
    b. Cosine

## Slide 54
  To solve a triangle using the law of cosines you must have either:
    three sides, or,
    two sides and an angle
B. Plane Trigonometry
  2. Trigonometric functions
    b. Cosine

## Slide 55
r
282.3 ft
163.9 ft
135.7 ft
  Example
    Compute the value of the angle ρ in the triangle:
    From the Law of Cosines:
B. Plane Trigonometry
  2. Trigonometric functions
    b. Cosine

## Slide 56
Tangent of an angle is not limited to ±1.0
  Range is ±(infinity)
  Repeats every 180°
  Asymptotic at 90°, 270°, ...
  There’s a Law of Tangents,
  but we generally don’t need it.
B. Plane Trigonometry
  2. Trigonometric functions
    c. Tangent

## Slide 57
U
L
V
Questions?