## Slide 1: Mentoring Mondays Measurement & Computation Errors
I. Numbers
  A. Type
  B. Communication
  C. Sig Fig
II. Measurement Errors
  A. Quality
  B. Error Tenets
  C. Error Sources
  D. Error Types
  E. Behavior
  F. Minimizing
III. Random Errors
  A. Basic Analysis
  B. Error Propagation
IV. Least Squares Adj
  A. Compared to Simplified Adj
  B. Complex Networks
  C. Random Errors Only
  D. Redundancies
  E. Weights
  F. Linear/Non-Linear
  G. Adjustment Statistics
Tonight
Jerry Mahun, PLS
Retired and a burden on my wife
jerry.mahun@gmail.com
jerrymahun.com

## Slide 2
B. Error Propagation; 1. Simple
  When combining measurements compute a third value, how do their errors affect the result?
    It depends on how they are combined.
  a. Error of a Sum
    Adding or subtracting values which are subject to errors.
      Example: A soil specimen is divided into three sample parts which are separately weighed. What is the error in the soil’s total weight?
Soil sample | Weight
1 | 56.2 gr ±0.15 gr
2 | 28.9 gr ±0.21 gr
3 | 41.6 gr ±0.11 gr
Total wt = 127.6 gr ± ______ gr

## Slide 3
B. Error Propagation; 1. Simple
  b. Error of a Series
      The same error occurring multiple times.
      Example: Each time they set up a level, a survey crew can determine an elevation difference to ±0.015 ft. What is their expected misclosure on this loop?

## Slide 4
B. Error Propagation; 1. Simple
  c. Error of a Product
    Two values with errors are multiplied or divided.
      A±EA, B±EB  A x B ±?
      Example: What is error in a rectangular parking lot’s area based on the measurements of its sides?
186.1’±0.83’
97.6’±0.57’

## Slide 5
D
Etsi
MSA: ±(C+P)
Eref
B. Error Propagation; 2. Combined
  a. Distance
    Manufacturer states an accuracy (MSA) for distance between the instrument and reflector, eg, ±(3 mm + 3 ppm)
    There are centering errors at the inst (Etsi) and ref (Eref)

## Slide 6
D
±0.005 ft
MSA:
±(3 mm + 3 ppm)
±0.01 ft
B. Error Propagation; 2. Combined
  a. Distance
    Example:
    TSI setup error: ±0.005 ft; handheld reflector centering: ±0.01 ft; 712.36 ft measured distance. MSA: ±(3 mm + 3 ppm)
See workbook for comps

## Slide 7
B. Error Propagation; 2. Combined
  a. Distance
    Also applies to GPS H and V components
Hrov
D
Hbase
MSA: ±(Ch+Ph)
±(Cv+Pv)
Vbase
Vrov
Hbase: base centering error
Hrov: rover centering error
Vbase: base elev error
Vrov: rover elev error

## Slide 8
B. Error Propagation; 2. Combined
  b. Angle
  Angles are more complicated because there are three points and a number of random error sources:
    Instrument resolution
    Instrument centering
    Target centerings at BS and FS points
    Target sightings
    Distances to BS and FS points
    Number of times the angle is measured.
EBS
EFS
TSI
DBS
DFS
resolution;
centering

## Slide 9
B. Error Propagation; 2. Combined
  b. Angle
  Each source has its own error propogation.
    These are combined to determine the total expected angle error.
EBS
EFS
TSI
DBS
DFS
D
resolution;
centering
TSI Point & Read
TSI Centering
Target Centering
Angle Error

## Slide 10
B. Error Propagation; 2. Combined
  b. Angle
  Example
    A TSI with DIN spec of 2 sec;
      centering error: ±0.005 ft
    BS & FS centering errors: ±0.005 ft & ±0.01 ft;
    BS & FS dists: 176 ft & 243 ft.
    Angle was measured 2 D/R to get 123°30’10”
    What is the expected error in the angle?
EBS
EFS
TSI
DBS
DFS
D
resolution;
centering
See workbook for comps

## Slide 11: Summary
Error Budget Management
  Errors can’t be eliminated but effects can be minimized
  Systematic errors
    Procedure
    Adjustment
    Computation
  Random Errors
    Appropriate equipment
    Knowledgeable personnel
    Careful measuring techniques
Understanding the origin of and how errors behave ensures accurate and reliable measurement results.

## Slide 12
A. Compared to Simplified Adjustments; 1. Adv/Disadv
  Advantages
    Models random errors better
    Able to deal with multiple unknowns simultaneously
    Easily incorporate redundant measurements – the more the merrier
    Can easily use mixed quality measurements - weights
    Can generate statistics for
      overall adjustment
      individual unknowns
  Disadvantages
    Computation intensive
    Statistics overload
    Easy to misuse
Most
squares
Least
squares

## Slide 13
B. Building Complex Networks
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
Simple network adjustment is possible
815.43
822.32
824.07’
Example: Even distribution
  Closure error at BM D = 814.07-824.04 = +0.03
  Corr’n per elev = -0.03/3 = -0.01
    Adj ElevQ = 815.43+(1)(-0.01) = 815.42
    Adj ElevT = 822.32+(2)(-0.01) = 822.30
    Adj ElevBM D = 824.07+(3)(-0.01) = 824.04 check

## Slide 14
B. Building Complex Networks
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
Simple network adjustment is possible
815.43
822.32
824.07’
Example: Even distribution
  Closure error at BM D = 814.07-824.04 = +0.03
  Corr’n per elev = -0.03/3 = -0.01
    Adj ElevQ = 815.43+(1)(-0.01) = 815.42
    Adj ElevT = 822.32+(2)(-0.01) = 822.30
    Adj ElevBM D = 824.07+(3)(-0.01) = 824.04 check
Drawback of Simple Adj:
  Random errors are treated systematically.

## Slide 15
B. Building Complex Networks
Simple network adjustment is cumbersome.
815.43
822.32
824.07’
Point Q has two different elevations.
How do we apply a simple adjustment so point Q has only one elevation?
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
815.38

## Slide 16
B. Building Complex Networks
Simple network adjustment is not possible.
815.43
822.32
824.07’
Point Q has two different elevations.
Point T has two different elevations.
How do we apply a simple adjustment so both points each have a single elevation?
815.38
+15.82’
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
822.34

## Slide 17
C. Random Errors Only
  Mistakes and systematic errors must be eliminated/compensated.
  Mistake: effect can be spread into other measurements
    Residual sizes and distribution.
BMA
BMB
BMC
BMD
Q
R
Mistake in line BMB-Q:
Affects other lines touching Q.
Lines into R not affected

## Slide 18
C. Random Errors Only
  Mistakes and systematic errors must be eliminated/compensated.
  Mistake: effect can be spread into other measurements
    Residual sizes and distribution.
BMA
BMB
BMC
BMD
Q
R
Mistake in line BMB-Q;
R & Q connected
Mistake affects:
  all lines touching Q
  line between Q & R
  possibly other lines touching R.
The more df, the harder to track down mistakes.
Most LSA software have blunder detection.

## Slide 19
C. Random Errors Only
  Systematic errors
    Residual sizes and distribution depend on:
      Error character: scale or additive constant
      Which measurements are affected
    Example: traverse misclosure
Incorrect temp & pressure in TSI
Wrong ppm multiplier for all lines – scale.
Incorrect refl constant
Each line changes the same additive amount regardless of length.

## Slide 20
C. Random Errors Only
  Systematic errors
Line |  |  | Distance | 
From | To | Azimuth | Unscaled | Scaled
A | B | 30 00 00 | 365.790 | 365.790
B | C | 325 33 52 | 354.520 | 354.520
C | D | 219 02 01 | 645.840 | 645.840
D | A | 104 12 35 | 437.640 | 437.640
Closure Error | 
Azimuth | Dist
320 22 41.39 | 0.099
Precision: 1/ | 18,145
Line |  |  | Distance | 
From | To | Azimuth | Unscaled | Scaled
A | B | 30 00 00 | 365.790 | 369.448
B | C | 325 33 52 | 354.520 | 358.065
C | D | 219 02 01 | 645.840 | 652.298
D | A | 104 12 35 | 437.640 | 442.016
Closure Error | 
Azimuth | Dist
320 22 41.39 | 0.100
Precision: 1/ | 18,145
Line |  |  | Distance | 
From | To | Azimuth | Unscaled | Scaled
A | B | 30 00 00 | 365.840 | 365.840
B | C | 325 33 52 | 354.570 | 354.570
C | D | 219 02 01 | 645.890 | 645.890
D | A | 104 12 35 | 437.690 | 437.690
Closure Error | 
Azimuth | Dist
335 41 27.17 | 0.121
Precision: 1/ | 14,946
Scale each distance by 1.01
Add 0.05 to each distance
Original traverse data

## Slide 21
D. Redundancies; 1. General
  Redundancy; aka Degree of freedom (df)
      df = m-n
        m: number of measurements
        n: number of unknowns
+15.82’
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
m | 3
n | 2
df | 1
m | 5
n | 2
df | 3

## Slide 22
D. Redundancies; 1. General
  Measurements must be independent.
      Not changing conditions allows mistakes & systematic errors repeatition.
A
Horiz
Horiz
B
eFS
eBS
LoS
LoS
(a)
A
Horiz
Horiz
B
eBS
eFS
LoS
LoS
(b)
Leveling
From a single set up:
  (a) BS A and FS B
  (b) BS B and FS A
Collimation error does not compensate.

## Slide 23
D. Redundancies; 1. General
  Measurements must be independent.
      Not changing conditions allows mistakes & systematic errors repeatition.
Leveling
As min, inst should be taken down & reset:
  (a) Balance BS & FS dists;
  BS A then FS B
  (b) Reset inst with BS/FS dists balanced;
  BS B then FS A
A
B
Horiz
Horiz
eFS
eBS
LoS
LoS
(a) Initial setup
A
B
eBS
eFS
Horiz
Horiz
LoS
LoS
(b) Reset

## Slide 24
D. Redundancies; 2. Vertical Network – 1D
  In leveling, an observation between two points is Σ(BS) – Σ(FS).
A
BM Dog
B
How many observations are needed to determine elevations of points A and B?
2
1
tp
tp
BS
FS
BS
FS
BS
FS

## Slide 25
D. Redundancies; 2. Vertical Network – 1D
  In leveling, an observation between two points is Σ(BS) – Σ(FS).
How many observations are needed to determine elevations of points A and B?
Two unknowns (ElevA & ElevB) so two observations are necessary.
Add a redundancy...
2
1
tp
tp
BS
FS
BS
FS
BS
FS
A
BM Dog
B
(1)
(2)

## Slide 26
D. Redundancies; 2. Vertical Network – 1D
  Each unknown elevation must be connected to the network by at least two observations for redundancy.
A
BM Dog
B
(1)
(2)
(3)
A
BM Dog
B
(1)
(2)
(3)
m | 3
n | 2
df | 1
m | 3
n | 2
df | 1
True redundancy
Pseudo redundancy
  Point B has only one observation.

## Slide 27
D. Redundancies; 3. Horizontal Network – 2D
  Each point in a horizontal network has two unknowns: N and E.
A
B
D
C
(2)
A
B
D
C
(6)
(4)
(8)
(3)
(7)
(5)
(1)
Traditional traverse
  Measure 4 angles and 4 distances: 8 obs
  Fix one point and one direction: 6 unk
  8-6 = 2 redundancies
  Simplified adj: Compass, Transit, or Crandall Rule
    ΣLat = 0
    ΣDep = 0
2 df allows 2 math checks

## Slide 28
D. Redundancies; 3. Horizontal Network – 2D
  Adding redundancy....
A
B
D
C
A
B
D
C
A
B
D
C
m | 10
n | 6
df | 4
m | 12
n | 6
df | 6
m | 8
n | 6
df | 2
6 dists
4 angles
8 dists
4 angles
8 dists

## Slide 29
D. Redundancies; 3. Horizontal Network – 2D
  Adding redundancy....
Because each point has two unknowns, it must be connected to the network by at least three measuements for redundancy.
A
B
D
C
A
B
D
C
A
B
D
C
m | 10
n | 6
df | 4
m | 12
n | 6
df | 6
m | 8
n | 6
df | 2
true
pseudo
true
6 dists
4 angles
8 dists
4 angles
8 dists

## Slide 30
E. Weights; 1. Vertical – Leveling
  Distance
  Set ups
K
J
tp
tp
BS
FS
BS
FS
BS
FS
dJK
wjk = 1/dJK
nJK = 3
wjk = 1/3
K
L
tp
BS
FS
FS
BS
dKL
wkl = 1/dKL
nKL = 2
wkl = 1/2

## Slide 31
E. Weights; 2. Horizontal
  w = 1/(σ2) = 1/(E2)
  Distances
  Angles & Directions
EBS
EFS
TSI
DBS
DFS
resolution;
centering
D
Etsi
MSA: ±(C+P)
Eref

## Slide 32
F. Linear/Non-Linear; 1. Vertical
  An LSA minimizes the sum of the squares of the residuals of the observations: Σ(v2)=min
  Vertical
    Unknowns are elevations
    Measurements are simple addition and subtraction
      ElevB = ElevA + BSA – FSB
    Simple math means LSA is a direct solution of simultaneous equations.
K
L
tp
BS
FS
FS
BS
dKL

## Slide 33
F. Linear/Non-Linear; 1. Vertical
  To minimize Σ(v2), an equation including a residual must be created for each measurement.
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’

## Slide 34
F. Linear/Non-Linear; 1. Vertical
  To minimize Σ(v2), an equation including a residual must be created for each measurement.
Line
BMA-Q:
Q-T:
T-BMD:
BMD-Q
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’

## Slide 35
F. Linear/Non-Linear; 1. Vertical
  To minimize Σ(v2), an equation including a residual must be created for each measurement.
Line
BMA-Q:
Q-T:
T-BMD:
BMD-Q
Rearrange the equations in terms of their residuals
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’

## Slide 36
F. Linear/Non-Linear; 1. Vertical
  To minimize Σ(v2), an equation including a residual must be created for each measurement.
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
Square each residual equation and add them
The function must be minimized for each unknown.
Take the partial derivative with respect to each unknown elevation and set equal to 0.

## Slide 37
F. Linear/Non-Linear; 1. Vertical
  To minimize Σ(v2), an equation including a residual must be created for each measurement.
Take partial derivatives and simplify
Two equations in two unknowns
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’

## Slide 38
F. Linear/Non-Linear; 1. Vertical
  To minimize Σ(v2), an equation including a residual must be created for each measurement.
Take partial derivatives and simplify
ElevQ = 815.404’
ElevT = 822.292’
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’

## Slide 39
F. Linear/Non-Linear; 1. Vertical
  If another measurement is added, its squared residual is added to the function.
-8.66’
+6.89’
+8.91’
T
BMA
806.52'
BMD
824.04'
Q
+1.75’
As before:
  Partial derivatives with respect to each unknown elevation are set equal to 0.
  Resulting simultaneous equations are solved to determine the unknown elevations.
+15.82’

## Slide 40
F. Linear/Non-Linear; 2. Horizontal
  Unknowns are coordinates
  Measurements are angles and distances.
  Position determination requires trig which is non-linear.
  LSA solution uses coordinate variation
    Start with approximate coordinates
    Compute and apply corrections
    Repeat until corrections are below a threshold
A
B
D
C

## Slide 41
F. Linear/Non-Linear; 2. Horizontal
  Distances
T’
A
T
vat
DAT
The residual is the difference between the measured distance and the distance computed from coordinates.
Four partial derivatives (one for each coordinate) of the residual squared:
dNA, dEA, dNT, dET are corrections for the initial coordinates.

## Slide 42
F. Linear/Non-Linear; 2. Horizontal
  Angles
The residual is the difference between the measured angle and the angle computed from coordinates.
Six partial derivatives (one for each coordinate) of the residual squared:
dNA, dEA, dNF, dEF, dNT, dET are corrections for the initial coordinates.
A
AzAF
T’
vfat
AzAT
F
bFAT
T

## Slide 43
F. Linear/Non-Linear; 2. Horizontal
  Distances
T’
A
T
vat
DAT
Corrections are combined at points common to angles and distance measurements.
If above a cutoff value, corrections are applied to the coordinates and the process repeated.
Needless to say, this can be quite a lot of calculations.
A
AzAF
T’
vfat
AzAT
F
bFAT
T

## Slide 44
F. Linear/Non-Linear; 2. Horizontal
  Networks
A
B
D
C
Combined
A
B
D
C
Trilateration
A
B
D
C
Triangulation
A
B
D
C
Traverse

## Slide 45
G. Adjustment Statistics
  1. Overall
    Standard Deviation of the Unit Weight, So
  2. Unknowns
    a. Vertical
        SElev
Adj Elev
±SElev
Adj’d Elev
+SElev
68%
-SElev

## Slide 46
G. Adjustment Statistics; 2. Unknowns
    b. Horizontal
        SN and SE
NP
-SNP +SNP
F(N,E)
EP
-SEP +SEP
F(N,E)
-SNP +SNP
F(N,E)
-SEP +SEP
Combined:
Bi-variate Distribution
Northing uncertainty
Easting uncertainty

## Slide 47
G. Adjustment Statistics; 2. Unknowns
    b. Horizontal
Error
Rectangle
N
E
+SN
-SE
+SE
-SN
P
N
E
+SN
+SE
-SN
P
-SE
Standard
Errors
N
E
a
b
Standard Error
Ellipse
Aza
The position is weakest in the direction of the semi-major axis, a. Its direction is Aza.
Position is strongest in the semi-minor axis, b, direction.

## Slide 48
G. Adjustment Statistics; 2. Unknowns
    b. Horizontal
`
Standard error ellipse represents a confidence interval of approx. 33-35%.
Because it is a bi-variate distribution, increasing the confidence requires using the F-Statistic which depends on the df.
`
35% CI
50% CI
95% CI
DF | F; 95 CI
1 | 199.5
2 | 19.0
3 | 9.55
4 | 6.94
5 | 5.79
10 | 4.10

## Slide 49
G. Adjustment Statistics; 2. Unknowns
    c. Adjustment Considerations
      Example adjusted traverse.
Lot 3
Error Ellipse
100x mag

## Slide 50
G. Adjustment Statistics; 2. Unknowns
    c. Adjustment Considerations
      Example adjusted traverse and adjacent independent traverse.
Lot 4
Lot 3
Error Ellipse
100x mag

## Slide 51
G. Adjustment Statistics; 2. Unknowns
    c. Adjustment Considerations
      Example adjusted traverse and adjacent independent traverse.
Lot 4
Lot 3
Magnified 300x
Error Ellipse
100x mag
Point | semi-major | semi-minor | Az
N Lot 3 | 0.842’ | 0.396’ | 86°42’
NE Lot 4 | 0.924’ | 0.309’ | 149°50’

## Slide 52
G. Adjustment Statistics; 2. Unknowns
    c. Adjustment Considerations
      (1) Pin cushion / monument nest?
0.50 sf
~0.6’
~0.8’

## Slide 53
G. Adjustment Statistics; 2. Unknowns
    c. Adjustment Considerations
      (2) Noise level?
0.50 sf
~0.6’
~0.8’

## Slide 54: Mentoring Mondays Measurement & Computation Errors
I. Numbers
  A. Type
  B. Communication
  C. Sig Fig
II. Measurement Errors
  A. Quality
  B. Error Tenets
  C. Error Sources
  D. Error Types
  E. Behavior
  F. Minimizing
III. Random Errors
  A. Basic Analysis
  B. Error Propagation
IV. Least Squares Adj
  A. Compared to Simplified Adj
  B. Complex Networks
  C. Random Errors Only
  D. Redundancies
  E. Weights
  F. Linear/Non-Linear
  G. Adjustment Statistics

## Slide 55: Mentoring Mondays Measurement & Computation Errors
I. Numbers
  A. Type
  B. Communication
  C. Sig Fig
II. Measurement Errors
  A. Quality
  B. Error Tenets
  C. Error Sources
  D. Error Types
  E. Behavior
  F. Minimizing
III. Random Errors
  A. Basic Analysis
  B. Error Propagation
IV. Least Squares Adj
  A. Compared to Simplified Adj
  B. Complex Networks
  C. Random Errors Only
  D. Redundancies
  E. Weights
  F. Linear/Non-Linear
  G. Adjustment Statistics
A Whole Lotta Stuff!